## Slide 1
Purchaser will strictly follow the approved concept plan and further sub-division will not be allowed without the approval of the Authority.
The Soil Tests of the proposed area will be got carried out.
SPECIAL BUILDING REGULATIONS FOR FINANCE & TRADE CENTER

## Slide 2: SPECIAL BUILDING REGULATIONS FOR FINANCE & TRADE CENTER
PROPOSED BYE-LAWS |  |  | 
Plot Size | Less than 25 Kanals | 25-50 Kanals | Above 50 Kanals
Height | As per Height fixed by the Civil Aviation Authority |  | 
Building Line | 40 feet | 40 feet | 50 feet
Ground Floor Coverage | 60 % | 60 % | 60 %
Rear | 15 feet | 15 feet | 15 feet
Both Side | 15 feet | 15 feet | 15 feet
Floor Area Ratio | 1:8 | 1:10 | 1:12
NOTE: Apart from Special Regulations, all other provisions of Prevailing Building Regulations shall remain applicable.

## Slide 3: SPECIAL BUILDING REGULATIONS FOR FINANCE & TRADE CENTER
PROPOSED PARKING REQUIREMENT | 
For Hotels | 1 Car Space for every 6 Rooms
 | 1 Car Space for every 1000 sq. ft. of Shopping Area
 | 1 Car Space for every 1200 sq. ft. of Office Area
Restaurant, Café & Banquet Hall | 1 Car Space for every 700 sq. ft. of Floor Area
Bank Square, Commercial & Corporate Office, Super Store, Health Tower and all Other Uses | 1 Car Space for every 1200 sq. ft. of Floor Area
Apartments | 1 Car Space for every 1500 sq. ft. of Floor Area
Masjid, Service Area | As per Building Regulations
The Maximum no. of Parking Basements shall not exceed 5 Basements The Gross Floor Area shall not include the area of Mechanical Plant Room, Electrical Sub-Station, Prayer Halls, Public Toilets, Stairs, Covered Parking and Circulation of Vehicles. |